## Slide 1: Introduction to Bluetooth Low Energy (BLE)
with
By: Yeo Kheng Meng (yeokm1@gmail.com)
https://github.com/yeokm1/intro-to-ble
Tech Talk Tuesdays @OMG (16 Feb 2016)
Friday Hacks #98 @NUS Hackers (2 Oct 2015)
Hackware v0.8 (9 June 2015)
Hackware v0.7 (13 May 2015)
Hackers and Painters (10 April 2015)

## Slide 2: About Me
Graduated from NUS Computer Science in 2015
Worked in 2 startups so far
  Both BLE-related

## Slide 3: Where I started from?
Innova Technology
  Makes anti-loss BLE tags with companion phone app
  “Protags”
Android Dev
2013 – 2014
  Era before Android officially supported BLE
  Fragmentation like you have never seen

## Slide 4: Where I am now?
Algoaccess
  Med-tech startup: targeting at eye-professionals
  Help them to retrieve, manage and process the data
  Roles: many….
  2014 - present

## Slide 5
How things work?
OD, OS, CYL…
OD, OS, CYL…

## Slide 6: Intro: Bluetooth Classic
The “conventional” Bluetooth
2.4GHz
Range: 1m - 100m (10mtypical)
Connection-oriented: audio, file transfer, networking
Reasonably fast data rate: 2.1 Mbps
Power consumption:
  High but still < Wifi < 3G

## Slide 7: Intro: BLE
Introduced in Bluetooth 4.0 specification (2010)
Also known as
  Bluetooth SMART
  Single-Mode
  Dual-Mode = Classic + Single-Mode
Target applications
  Wireless battery-powered sensors eg. heart rate, thermometer, fitness
  Location tracking and information serving eg. iBeacons
Requirements for target applications
  Low-power
  Low-cost
  Low bandwidth: ~100 kbps
  Low latency: Connectionless (fast setup and teardown of connection in ~10ms)
How?
  Radio chip off most of the time
  Small packets
    MTU: 20 bytes/packet for application
    Less time transmitting -> less heat -> no need compensatory circuits -> save more power

## Slide 8: Bluetooth Classic vs SMART
An actual battery-life comparison
Innova’s anti-loss products
vs
Protag G1 (Classic)
Released: 2012
Battery Capacity: 3.7V, 270mAh
Battery Life: 1 - 2 weeks
Protag Elite (SMART)
Released: 2013
Battery Capacity: 3.7V, 150mAh
Battery Life: 6 months to 1 year

## Slide 9: Wireless constraint triangle
Power usage ↓
Range↑
Speed↑
*Positions are for relative comparison only, they are not absolute
3G/4G
RFID/NFC
Other factors not mentioned
Cost
  Royalties
  Manufacturing
Adoption rate
Topology support
  Mesh
  Star
Zigbee
BT Classic
802.11 n/ac
5Ghz
802.11 b/g/n
2.4Ghz
BLE

## Slide 10: What’s on the agenda?
BLE theoretical concepts*
  Device Role 1: Broadcaster vs Observer
  Device Role 2: Central vs Peripheral
  OS/Device Compatibility
  UUID, Attribute, GAP, GATT, Service, Characteristic, Descriptor
  BLE connection procedure
Peripheral hardware design and software planning
  Functional requirements
  Hardware setup
  Peripheral architecture plan
Execution
  Arduino (C)
  Central architecture plan (iOS and Android)
  iOS (Swift)
  Raspberry Pi (JavaScript)
  Android (Java)
Issues and tips
  General issues
  iOS
  Android (past, today, production app tips)
BLE layer model and packet concepts
BLE Sniffer
Further reading
Extra questions
* Exact definitions are not used to aid ease of explanation

## Slide 11: 1a. Device Role 1: Broadcaster vs Observer
Observer 1
Broadcaster 1
Advertises
aka Beacon-mode
One-way advertisement information transfer from broadcaster to observer(s)
Observer 2
Observer 3
Broadcaster 2

## Slide 12: 1b. Device Role 2: Central vs Peripheral
Central
Peripheral
Advertises
Connects to
Platform | Terms they prefer (generally mean the same thing)
iOS | Central/Peripheral
Android | Client/Server
Chipset manufacturers | Master/Slave

## Slide 13: 1b. Device Role 2: Central vs Peripheral
Source: https://learn.adafruit.com/assets/13826
Central can connect to many peripherals at the same time
Peripheral can connect to only one central at any one time.

## Slide 14: 1c. OS/Device Compatibility
Observer/Central | Broadcaster/Peripheral
iOS 5 Windows 8 Mac OS X 10.7 (Lion) Linux kernel 3.5 Bluez 5.0 Android 4.3 (Jelly Bean MR2) X - Nexus 7 (2012), 10* X - Galaxy Nexus* Hardware chipsets CC2540 CSR1010 NRF51/52 | iOS 6 Windows 10 Mac OS X 10.9 (Mavericks) Linux kernel 3.5 Bluez 5.0 Android 5.0 (Lollipop) X - Nexus 4, 5, 7 (2013)* ✔ - Nexus 6, 9, 5X, 6P Hardware chipsets CC2540 CSR1010 NRF51/52 NRF8001
*Hardware capable but not certified by Bluetooth SIG-> disabled in OS
, custom ROMs may enable these BLE features

## Slide 15: 1d. UUID, Attribute
Universally Unique Identifier (UUID)
  128-bit eg. “12345678-ABCD-EF90-1234-00805F9B34FB”
  To ensure practical uniqueness if randomised
  2128 = 3.4 x 1038
  16-bit for Bluetooth Special Interest Group (SIG) defined services/characteristics/descriptors
    Combined inside Bluetooth Base UUID
    0000xxxx-0000-1000-8000-00805F9B34FB
Attribute
  Anything that has a UUID
  Refers to Services, Characteristics and Descriptors

## Slide 16: 1d. GAP, GATT (defined by Peripheral)
Generic Access Profile (GAP) or Advertising
  Information advertised to central before connection
  Name of peripheral
  Is it connectable?
  Supported features (services)
Generic Attribute Profile (GATT)
  How to exchange data once connected
  Identifies Services, Characteristics and Descriptors
*Both GAP and GATT are theoretical concepts, you don’t usually see those terms in coding APIs.

## Slide 17: 1d. Service, characteristic, descriptor (All these are part of a peripheral’s GATT)
Service
  16-bit SIG services: Battery, Heart rate, Immediate Alert, Tx Power
  128-bit UUID for custom services
  Collection of characteristics
Characteristic
  Holds a value: String, Int, Char…..
  Can take on multiple properties:
    Read: Central can read this value directly
    Write: Central can write/change this value and be notified if executed successfully
    WriteWithoutResponse: Central just “fire and forget”
    Notify: Central gets alerted if the value has changed
    Others: Broadcast, Indicate, SignedWrite, QueuedWrite, WritableAuxiliaries
  Collection of optional descriptors
Descriptor: usually optional
  Holds a value
  Used to describe a characteristic (meta-data)
  Special case: Client Characteristic Configuration Descriptor (0x2902)
    Usually automatically created for characteristics with “notify” property

## Slide 18: 1d. Service, characteristic, descriptor
GATT
Service1
Service2
Characteristic1
Properties: Read, Notify
Characteristic1
Properties: Read, Write
Descriptor1
Characteristic2
Properties: WriteWithoutResponse
Descriptor1
Descriptor2

## Slide 19: 1e. BLE connection procedure
Observer
Broadcaster
Central
Peripheral
Broadcasts advertisement packets (GAP)
2.5. Connection attempt
Connect success
Discover services
Services data (GATT)
Discover characteristics
Characteristics data (GATT)
1. Scanning
Advertising
2. Received advertisement packet
Connected success, stops advertising
3. Connect success,
now lets find out more
Send back services info
4. Services discovered, lets dig deeper
Send back characteristics info
5. Discovery completed, ready to use peripheral
Discover descriptors (usually optional)

## Slide 20: 2a. Functional Requirements
Connection Status
  Red LED to indicate no connection
  Green LED to indicate active connection with central
Controllable via BLE
  Let central toggle blue LED
  Let central toggle yellow LED
  Button to trigger sending data back to central

## Slide 21: 2b. Hardware setup (Arduino)
Arduino Parts list
Arduino Uno R3
RedBearLab BLE (Single-Mode) Shield v.1.1
  (Not shown in schematic)
  NRF8001 chipset
Red LED
Green LED
Blue LED
Yellow LED
4x 220ohm resistors
Push Button

## Slide 22: 2b. Hardware setup (Raspberry Pi)
Raspberry Pi Parts list
Raspberry Pi 2 Model B
IOGear GBU521 USB BLE (Dual-Mode) adapter
  BCM20702 chipset
Red LED
Green LED
Blue LED
Yellow LED
4x 220ohm resistors
Push Button
10k ohm pull-down resistor

## Slide 23: 2. Peripheral Architecture Plan
Service 1 (UUID : "12345678-9012-3456-7890-123456789012“)
Characteristic 1 (LED)
Value type: char (1-byte character)
UUID : “00000000-0000-0000-0000-000000000010”
Properties: Read, WriteWithoutResponse
Characteristic 2 (Button)
Value type: String
UUID : “00000000-0000-0000-0000-000000000020”
Properties: Read, Notify
LED characteristic
Toggles blue LED if central writes “b”
Toggles yellow LED if central writes “y”
Button characteristic
Notifies central if button is pressed
Sends back incrementing number
Generic Attribute Profile (GATT)
Generic Access Profile (GAP)
Field | Value
Device name (general) | YKM’s Arduino (Not accessible via Android APIs)
Local name (specific): | Intro to Arduino BLE
isConnectable | Yes
Services | 1 service: UUID = "12345678-9012-3456-7890-123456789012“

## Slide 24: 3a. Arduino code
Programming Language: C
Arduino IDE 1.6.7
Libraries Used
  ble-sdk-arduino for NRF8001 (By Nordic)
    https://github.com/NordicSemiconductor/ble-sdk-arduino
  arduino-BLEPeripheral (By Sandeepmistry)
    Abstraction over ble-sdk-arduino
    https://github.com/sandeepmistry/arduino-BLEPeripheral

## Slide 25: 3b. Central architecture plan (iOS and Android)
MainActivity/ViewController
(UI)
BLEHandler
(Deals with platform’s BLE APIs)
BLEHandlerCallback** Interface/Delegate
Calls functions
Returns results*
*BLE APIs are asynchronous in nature.
**Use BLEHandlerCallback to avoid tight coupling between UI and BLEHandler
implements

## Slide 26: 3c. iOS Code
Platform
  Device: iPod Touch 6G
  OS: iOS 9.2.1
Programming Language: Swift 2
Xcode 7.2.1

## Slide 27: 3b. Raspberry Pi code
Platform
  Device*: Pi 2 Model B
  OS*: Arch Linux ARM
Programming Language: Javascript
Framework used: Nodejs
Nodejs BLE Library
  Bleno (by Sandeepmistry again)
  Abstraction over Linux’s Bluez stack/API
  Aggressive maintenance
  https://github.com/sandeepmistry/bleno
Why not others, Python, Go or C?
  Bleno is more “mature” and “easier to use”
*Others will work too

## Slide 28: 3c. Android code
Platform
  Device: Nexus 5
  OS: Android 6.0.1
Programming Language: Java
Android Studio 1.5.1

## Slide 29: 4a. General Issues
  Limit data transfer to 20-byte chunks
Peripheral
  Characteristics support UTF-8 values
    I use ASCII for Arduino compatibility, but UTF-8 is generally safe
Central
  All callbacks from BLE APIs are not on UI thread
  Must rescan upon Bluetooth/phone restart
    Existing CBPeripheral (iOS) and BluetoothDevice (Android) references becomes invalid

## Slide 30: 4b. iOS issues
Cannot retrieve Mac Address
  Generated UUID specific to iOS device
  Identification issues across iOS devices /Android
  Solution:
  Peripheral embeds Mac Address in advertisement (GAP) data
      Manufacturer data field (Innova Technology)
      In device/local name fields (Algo Access)
Aggressive caching of GATT data
  Receive out-of-date GATT data during peripheral development
  Solution:
    Restart iOS’s Bluetooth after every change in peripheral software/firmware
Max number of BLE connections
  ~20 (online anecdotes)

## Slide 31: 4c. Android issues (the past)
Before Android 4.3 (July 2013)
  Fragmentation hell
  Proprietary Libraries by OEMs, Android <= 4.2
    Samsung (quite reliable)
    HTC – buggy, unreliable
    Motorola (reliable but conflicts with Android 4.3)
  Architecture issues
Testing issues

## Slide 32: 4c. Android issues (today)
OS fragmentation
74.2% of Android devices support BLE
Few support peripheral mode: 35.3% minus Nexus 4, 5, 7 (2012/2013)

## Slide 33: 4c. Android issues (today)
APIs considered new, some functions are buggy
Frequent connection drops (< 5.0)
Max BLE connections:
  Software cap in Bluedroid code: BTA_GATTC_CONN_MAX, GATT_MAX_PHY_CHANNEL
  Android 4.3: 4
  4.4 - 5.0+: 7
No API callback to indicate scanning has stopped
  Scan supposed to be indefinite by API specification, but some phones stop scan after some time
  Known offender: Samsung
  Solution: Restart scan at regular intervals
Different scan return result behaviours (See further reading)
  Some phones filter advertisement results, some phones do not. (4.3 and 4.4 only)
Bugs on (Samsung) phones at least < 5.0
  Scan using service UUID filtering does not work -> no results returned
  connectGatt() must be called from UI thread
Slow LE initial discovery and connection time
  HTC seems to have this issue
A high-level view on issues collated by Anaren
  https://atmosphere.anaren.com/wiki/Android_Issues_With_Bluetooth_Low_Energy
A more comprehensive list of issues has been collated by iDevicesInc
  https://github.com/iDevicesInc/SweetBlue/wiki/Android-BLE-Issues
  May be able to overcome using: https://github.com/iDevicesInc/SweetBlue
  Free for non-commercial use

## Slide 34: 4c. Tips for production Android app
Use Nexus (reference phone) or Motorola for initial development
Get many models from differing manufacturers

## Slide 35: 5. BLE layer model
Link-layer:
  Defines how two BLE devices communicate. Advertising, Scanning, Connecting, Packet Format
  Convention is to use Master/Slave instead of Central/Peripheral
L2CAP:
  Segmentation and reassembly of packets
  4-byte header
  23 bytes for MTU
  Protocol multiplexing
    0x0004: ATT Channel (usually used)
    0x0005: LE signalling
    0x0006: Security Manager
ATT
  Action to be taken (Read/Write/…)
  1-byte instruction opcode
  2-byte handle (ID of relevant service/characteristic/descriptor)
  20-byte MTU for application
(L2CAP)
Source: https://developer.bluetooth.org/KnowledgeCenter/PublishingImages/GATT_stack.png
(ATT)
(Master/Slave)
(GAP)
(GATT)

## Slide 36: 5. BLE Data Link-layer Packet Structure
Field size (bits) | 8 | 32 | 8 | 8 | 0-296 | 24
Field name | Preamble (Alternating bits for receiver calibration) | Advertising /Data Access Address | Header | Length | Payload | CRC
Only 1 packet structure
Two types of packets
  Advertising
    Advertising Access Address: Always 0x8E89BED6
  Data
    Data Access Address: Random for every connection
      Allows Master/Slave to distinguish packets associated with a connection
      Mac Address no longer used for data packets
    Usually carries L2CAP/ATT payload
PDU header format for Advertising != Data
Protocol/Packet Data Unit (PDU)
LSB

## Slide 37: 6. BLE Sniffer
Adafruit Bluefruit LE Sniffer
Based on Nordic nRF51822
Required software:
  Nordic nRF Sniffer (Windows-only)
  Results piped to Wireshark
Alternative: Ubertooth One

## Slide 38: 6. Sniffer: Advertising
ADV packets’ payload contains GAP data:
  Mac Address
  Service UUID
  Supported Bluetooth features: Dual/Single mode
  TX Power (Optional)
  Name (Optional)
PDU/Advertising Type:
  4-bit field determines type of ADV Packet
Slave is connectable
  0000: ADV_IND (Undirected connectable mode)
    No need to connect in a hurry
  0001: ADV_DIRECT_IND (Directed connectable mode)
    To indicate to master that slave wants to be connected quickly.
    Max 1.28s in this mode
Slave is not connectable
  0010: ADV_NONCONN_IND (Not scannable)
    Will not respond to scan (SCAN_REQ) requests for more info
  0110: ADV_SCAN_IND
    Will response to SCAN_REQ with SCAN_RSP
Source: BLE: The Developer’s Handbook by Robin Heydon, pg82
Link layer format
0x8E89BED6

## Slide 39: 6. Sniffer: Scan
ADV Packets may not hold all advertising info
  Central can issue SCAN_REQ to ask for more
0011: SCAN_REQ (Active Scan Request)
  Master -> Slave
  Ask peripheral for complete GAP data
0100: SCAN_RSP (Response)
  Slave -> Master
  Contains slave’s name, TX power, …

## Slide 40: 6. Sniffer: Connection
PDU Type:
0101: Connect_REQ (Connect Request)
  Master -> Slave
  Master selects and sends a random data access address
    Link-layer data -> Access address field
0110: Empty PDU (Keep-alive packet)
  Sent at connection interval between Master <-> Slave
  Filter "not btle.data_header.llid==0001” to ignore in Wireshark

## Slide 41: 6. Sniffer: Data Packets
Payload usually contains L2CAP/ATT data
Link-layer identifier (LLID) – 2 bits
  11 : Control Packet
  10 : Start/Full Packet
  01: Continuation of fragmented packet
If LLID == 11 (Control Packet)
  Header format changes to have control and error fields
  Does not contain L2CAP/ATT payload data
  0x0c: LL_VERSION_IND: Negotiate supported Bluetooth Spec
  0x01: LL_CHANNEL_MAP_REQ: Channel hop (Master -> Slave)
  0x02: LL_TERMINATE_IND: Terminate connection
Source: BLE: The Developer’s Handbook by Robin Heydon, pg83
Link layer format

## Slide 42: 6. Sniffer: Discover services/characteristics
ATT opcodes
0x10: Read by Group Type Request (Discover Services)
  Master -> Slave
0x11: Read by Group Type Response
  Slave -> Master
  Returns Services Requested
0x08: Read by Type Request (Discover Characteristics)
  Master -> Slave
0x09: Read by Type Response
  Slave -> Master
  Returns Characteristics Requested
You may notice some “hidden” services during sniffing
Generic Access Service: 0x1800 (Contains generic info, name, type etc about peripheral)
Generic Attribute Service: 0x1801 (I don’t know what this is)

## Slide 43: 6. Sniffer: Data transfer
0x52: Write Command (Write to Characteristic)
  Master -> Slave
0x1b: Handle Value Notification (Notify Characteristic Changed)
  Slave -> Master

## Slide 44: 7. Further reading
BLE 4.0-4.1 Security (Passive) Weaknesses (19:58 to 23:14)
  Video: https://www.usenix.org/conference/woot13/workshop-program/presentation/ryan
  Paper: https://lacklustre.net/bluetooth/Ryan_Bluetooth_Low_Energy_USENIX_WOOT.pdf
In-depth introduction by Nordic Semiconductor
  https://www.youtube.com/watch?v=BZwOrQ6zkzE
Acceptable types of Characteristic values
  https://developer.bluetooth.org/gatt/descriptors/Pages/DescriptorViewer.aspx?u=org.bluetooth.descriptor.gatt.characteristic_presentation_format.xml
BLE Sniffer (by Adafruit)
  https://learn.adafruit.com/introducing-the-adafruit-bluefruit-le-sniffer
Android 4.3 BLE unstable
  http://stackoverflow.com/questions/17870189/android-4-3-bluetooth-low-energy-unstable
Android different scan results behaviour
  http://stackoverflow.com/questions/19502853/android-4-3-ble-filtering-behaviour-of-startlescan
Android 5.0 BLE APIs improvement vs 4.3
  https://www.youtube.com/watch?v=qx55Sa8UZAQ
High-level Android Issues collated by Anaren
  https://atmosphere.anaren.com/wiki/Android_Issues_With_Bluetooth_Low_Energy
Lower-level Android issues collated by iDevicesInc
  https://github.com/iDevicesInc/SweetBlue/wiki/Android-BLE-Issues
BLE Advertising Packet Format
  http://j2abro.blogspot.sg/2014/06/understanding-bluetooth-advertising.html
Bluetooth Core (Adopted) Specification
  https://www.bluetooth.org/en-us/specification/adopted-specifications

## Slide 45: 8a. Can Peripheral prevent unwanted connections from unknown Central?
Not possible to block connection attempt
But peripheral can disconnect the central after connected
  Wait for key-exchange
  Mac address whitelist
Disconnect APIs
  arduino-BLEPeripheral
    blePeripheral.disconnect();
  Bleno
    bleno.disconnect();

## Slide 46: 8b. Who defines the attributes?
Peripheral always defines the attributes
  Services, characteristics and descriptors
Then why did I do this on the Central?
Android:
iOS:
Reason:
  I hardcoded the characteristic UUIDs to address the characteristics directly since I already know their purpose

## Slide 47: 8c. BLE Security?
Bluetooth pairing
< Bluetooth 4.2:
  Strongly discouraged to use native BLE security features Key-exchange protocol weakness
  See video in Further Reading
Security issues fixed in 4.2 (Dec 2014)
  But many devices in the market have not adopted this

## Slide 48: 8d. Data loss from using writeWithoutResponse instead of write property?
Possibility exists but unlikely to happen in practice
Rough Analogy:
  write vs writeWithoutResponse -> TCP vs UDP
  Possible to lose data if central sends faster than peripheral can process